## Slide 1
OPWC
LBR
Local Major
SIB Loan
Local Match
Grant
TRAC

## Slide 2
Bridge Project Funding Examples August 12, 2026
Warren County
Warren
Warren County Engineer’s Office
Kurt E. Weber, P.E., P.S.
Warren County Engineer
210 W. Main Street, Lebanon, OH 45036
Phone: (513) 695-3301 Fax: (513) 695-7714
https://engineer.warrencountyohio.gov/
Warren County Engineer’s Office Staff
16 Employees
7 Engineers
6 Inspectors or Technical Positions
3 Administrative Positions

## Slide 3
Bridge Project Funding Examples August 12, 2026
King Avenue Bridge Replacement over Little Miami River
EXISTING CONDITIONS
Bridge: Existing 6-span concrete box beam bridge deteriorated to a point of posting for reduced weights
Roadway: Existing roadway had narrow lanes and shoulders, steep vertical profile down to the bridge, and sharp horizontal curves on both bridge approaches
Trail: Existing trail had dangerous at grade road crossing near a curve and did not have an improved access or parking area

## Slide 4
Bridge Project Funding Examples August 12, 2026
King Avenue Bridge Replacement over Little Miami River
2-span steel girder bridge over National Scenic River (total length 520 ft) with stub abutments on H-Piles and wall pier on drilled shafts
Bridge accommodates 2 lanes of traffic with wider shoulders and a 12 ft shared use path
Improved roadway geometry at both bridge approaches
Roundabout at entrance to trail parking lot and new development
Precast arch structure now provides grade separation for Little Miami Scenic Trail

## Slide 5: Project Funding
Bridge Project Funding Examples August 12, 2026
King Avenue Bridge Replacement over Little Miami River
Largest WCEO project constructed to date ($22,041,788.13)
$5M in Federal Local Bridge Replacement Funds (LBR)
$6.27M in Federal Surface Transportation Block Grant Funds (STBG)
$800,000 in Ohio Public Works Commission Funds (OPWC)
$3M in Congressional Directed Spending (CDS)
Outside funding kept our local portion at $4,045,669.50, just under 20% of the total construction cost

## Slide 6: Congressional Directed Spending (CDS)
Bridge Project Funding Examples August 12, 2026
King Avenue Bridge Replacement over Little Miami River
WCEO was contacted for interest in transportation construction funding by Steve Chabot’s Office
Staff member followed up with us and provided funding details
Application was simple and straightforward
Several members from Chabot’s staff came to Warren County for a project site visit and interview
About a year after the application was submitted our project was awarded $3M
Thankfully, we still had enough construction left to fully use the maximum $3M award
No real suggestions with his type of funding other than reaching out to your local representatives and ODOT Districts on an annual basis

## Slide 7
Bridge Project Funding Examples August 12, 2026
Mason-Morrow-Millgrove Road Bridge Replacement
EXISTING CONDITIONS
Bridge: Existing single span concrete box beam bridge deteriorated to a point of posting for reduced weights
Trail: Mason Sports Park did not have pedestrian access from several neighborhoods to the east

## Slide 8
Bridge Project Funding Examples August 12, 2026
Mason-Morrow-Millgrove Road Bridge Replacement
Single span (85 ft) prestressed concrete I-beam superstructure on semi-integral abutments resting on drilled shafts
Bridge accommodates 2 lanes of traffic and a 12 ft shared use path
Access to Mason’s Sports Park over Muddy Creek from nearby neighborhoods

## Slide 9: Project Funding
Bridge Project Funding Examples August 12, 2026
Mason-Morrow-Millgrove Road Bridge Replacement
Overall Joint Project Construction Cost ($2,006,278.41)
City of Mason’s Portion for Shared Use Path ($521,356.44)
$882,000 in Ohio Public Works Commission Funds (OPWC)
$140,342.52 Grant Reimbursement from ODOT’s Office of Jobs & Commerce
Outside funding kept our local portion at $462,579.45, just under 20% of the total construction cost

## Slide 10: ODOT’s Office of Jobs & Commerce
Bridge Project Funding Examples August 12, 2026
Mason-Morrow-Millgrove Road Bridge Replacement
WCEO connected with our Regional Manager of ODOT’s Jobs & Commerce
We answered a few questions by email and provided a construction cost estimate
Entire process was quick and painless
Within two months we received the Award Letter for roadway and bridge portion of work, as shared use path work was not eligible
ODOT was barely involved in the project with this type of state grant
We provided copies of Contractor pay estimates and proof of our payments for state reimbursement
Jobs & Commerce grants can only be used when there are new or retained jobs in a JobsOhio industry sector and a capital investment is being made by the company
Projects can’t be related to residential or retail
Each ODOT District has a regional manager that can help discuss projects and determine eligibility

## Slide 11
Bridge Project Funding Examples August 12, 2026
Franklin County
County Engineer Adam W. Fowler, P.E., P.S.
Maintenance Responsibility +1.3M Population
850 Lane Miles of Roadway 357 Bridges
Current Bridge Projects With Outside Funding 4 Local Major Bridge Program 3 Ohio Publics Works (OPWC) 1 MORPC Attributable Funding 2 Local Bridge Program (LBR/BFP)
Credit Bridge
$35 million
In Current Bridge Funding

## Slide 12
Bridge Project Funding Examples August 12, 2026
Franklin County Budget
Chart: 2025 Revenue - Actual
| $35.7M Motor Vehicle Registrations | $18.2M State & Federal Grants | $8.5M Other Government Revenues | $4M Motor Vehicle Gas Tax | $2M Other Revenues
 | 35719241.4 | 18260677.82 | 8526810.86 | 3956771.8 | 2030643.62
Chart: 2025 Expenditure - Actual
| $16.4M Payroll Services | $6.4M Fringe Benefits | $12.4M Materials & Services | $36M Capital Expenses | $436K Debt Services
 | 16446281.32 | 6370173.34 | 12442683.78 | 36161499.92 | 436511.3
2025 Total Revenue
$68,494,146
2025 Total Expenditures
$71,857,150

## Slide 13
Bridge Project Funding Examples August 12, 2026
Force Account Projects
Old Haughn Road over Holton Run
Project Cost: $240,047 Force Account Cost: $176,481
Roberts Road over Morris Ditch
Project Cost: $255,356 Force Account Cost: $235,687

## Slide 14
Bridge Project Funding Examples August 12, 2026
Force Account Projects
Winchester Pike over Coble Bowman Ditch
Project Cost: $240,047 Force Account Cost: $240,594
Pontius Rd over Tributary to Little Walnut Creek
Project Cost: $150,186 Force Account Cost: $150,186

## Slide 15
Bridge Project Funding Examples August 12, 2026
2025 Force Account Project Final Costs
BID CONTRACT WORK

## Slide 16
Bridge Project Funding Examples August 12, 2026
Cooper Road over Noble Run

## Slide 17
Bridge Project Funding Examples August 12, 2026
Force Account Projects
Force Account abutment work
Superstructure and abutment cap demo
Rebuild abutment seats
General Bridge Maintenance Contract
Install NEXT E Beams on converted semi-integral abutments
Pour concrete deck on a skewed, superelevated, vertical curve

## Slide 18
Bridge Project Funding Examples August 12, 2026
Marlane Drive over Marsh Run
2027 FULL REPLACEMENT
Redi-Rock abutments
Superstructure TBD
Force Account approx. $250k
($150k encumbered)
Gen Bridge Maintenance Contract approx. $500k

## Slide 19
Bridge Project Funding Examples August 12, 2026
Mahoning County
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run
Notes: Good Morning everyone and thank you for the opportunity to discuss our a few bridge projects recently completed in Mahoning County Engineer.

## Slide 20: PROJECT LOCATION
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run
Notes: The Mahoning Avenue Bridge over Morrison Run is located ½ mile west of S.R. 45 is an east-west thoroughfare in Jackson Township in the main Industrial Corridor

## Slide 21: PROJECT LOCATION
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run

## Slide 22: PROJECT FUNDING
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run
The total cost of the bridge replacement project was $417,392
(33%) funded by U.S. EDA $137,739
(19%) funded by OPWC $79,304
(8%) funded by MCTID $33,391
(18%) funded by TIF $75,131
(22%) funded by Sales Tax $91,827

## Slide 23: PROPOSED WORK
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run

## Slide 24: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run
View of surface (left) and view underneath looking north (right)

## Slide 25: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run
View of underneath looking east (left) and view looking south (right)

## Slide 26: CONSTRUCTION PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run
Installation of 20x6 precast box culvert & placement of LSM backfill along with Type 2 & Type 3 waterproofing

## Slide 27: CONSTRUCTION PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run
Poured outlet wingwalls (north side) & Rock Channel Protection on North end

## Slide 28: COMPLETED BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run

## Slide 29: COMPLETED BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Mahoning Avenue Industrial Corridor Bridge over Morrison Run

## Slide 30
Bridge Project Funding Examples August 12, 2026
Mahoning County
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR

## Slide 31: PROJECT LOCATION
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
Notes: The Market street bridge is the main southern access point into downtown Youngstown and some of you may know that this route used to be SR 7 into and through the downtown prior to it being rerouted across Williamson Avenue to US 62

## Slide 32: LOCATION MAP
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
Notes: As you can see in this picture the Covelli Centre is to the east of the bridge, and it’s the home of the Youngstown Phantom Hockey team and to the west of the bridge is the Youngstown Foundation Ampitheatre where several great outdoor concerts have been held and all of the grassy area between these two venues is called Ween Park. This project started out as a deck maintenance project that would not involve the railroad in any way.

## Slide 33: PROJECT FUNDING
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
The original Major Bridge funding grant was $1,878,000 (49%) and we were using $1,955,221 (51%) Bridge Sales Tax.
The final construction cost was $3,835,308 and ODOT paid $3,536,949 (92%). We paid $186,155.22 (8%) with Bridge Sales Tax.
Notes: ms consultants was the design engineer for this project as well as the previous maintenance project completed in 2014. This project started out with the intent to patch the deck, replace the lighting and add safety fencing. Thanks to the passage of the county sales tax for roads & bridges we now had the leverage to apply for funding to expand the scope by giving us a revenue stream to cover the local match.
At the completion of the in-depth inspection by ms consultants, the project scope was expanded due to finding additional maintenance work items needing to be addressed. The County was successful in securing the Local Major Bridge Funding (LMB funding). Had the county not been successful in passing the sales tax which is dedicated to roads & bridge, we would have either pushed the maintenance work into another year in hopes of securing LMB funds in a future fiscal year or reduce the scope and use our local funding to do only those items that are deemed most critical to extending the life of the bridge. As you can see by the original funding, the local match would have been almost $2 Million on this bridge.

## Slide 34: EXISTING BRIDGE
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
Constructed in 1981
Continuous A588 (weathering steel) welded plate girders with reinforced concrete deck and cap-and-column piers & abutments
13 Spans = 191’, 210’, 168’, 99.33’, 111’, 111’, 111’, 116’, 116’, 93’, 85’, 85’, 78.17’ = +/- 1,574’
Skew = None
Design Loading = HS20-44 & Alt. Military Loading
Notes: The bridge was built in 1981 has 13 spans comprising 4 units with an overall length of 1,574’ which makes it the 6th longest county bridge in the state of Ohio out of the approximately 25,300 bridges maintained by the 88 Ohio County Engineer’s. The width varies from 52’ to 68’.

## Slide 35: PROPOSED WORK
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
Remove and replace existing bridge lighting
Replace existing strip seals at expansion joints
Replace existing elastomeric compression seal and joint armor at North Abutment
Install new vandal protection fence (8’ tall to allow future snooper inspections)
Install new micro silica modified concrete overlay (at Units 3 & 4 only)
Patching concrete deck (at Units 1 & 2)
Patching concrete abutments and piers
Re-face parapets
Repair structural steel & perform repair painting
Repair drainage system (scuppers & downspouts)
Seal bridge deck with gravity fed resin (Units 1 & 2)
Seal concrete substructures and parapets
Provide new pavement striping on bridge
Notes: As you'll see in the upcoming pictures, the existing bridge lighting needs to be replaced and actually 3 poles have already fallen over and had to be removed, the seals and expansion joints all need to be replaced, Units 3 & 4 will receive a new silica modified concrete overlay as these 2 units comprise the majority of the deck repair area. Units 1 & 2, the parapets, abutments & piers will be patched and sealed, the drainage system will be repaired, some structural steel will be repaired and painted and unfortunately we have a need to place fencing on the bridge due to the fact that three people jumped from the bridge over the last 7 years.

## Slide 36: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
Areas of delaminated or unsound concrete on top surface of deck

## Slide 37: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View of Expansion Joint showing tears in elastomeric strip seal (typ. of all existing strip seals)

## Slide 38: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View of missing light pole (typical of three locations on bridge)

## Slide 39: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View of light pole pilaster with spalled concrete and corroded reinforcing steel (typ. of several locations)

## Slide 40: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View of cracked and spalled concrete parapet and exposed and corroded reinforcing steel

## Slide 41: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View of top of Pier #3 showing delaminated and spalled concrete with exposed reinforcing steel

## Slide 42: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View of nearly 100% section loss to horizontal angle at first cross frame to the north of Hinge #1

## Slide 43: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View from below deck (looking up) showing leaking drainage system

## Slide 44: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View of broken weld between end diaphragm angle and back of channel (at Hinge #2)

## Slide 45: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View of leaky compression seal at expansion joint at Fwd. Abutment

## Slide 46: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
Steel Corrosion at Beam at South Abutment

## Slide 47: EXISTING BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR
View of Pier #3 showing delaminated concrete and drainage system deficiency

## Slide 48: COMPLETED BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR

## Slide 49: COMPLETED BRIDGE PHOTOS
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR

## Slide 50: THANK YOU!
Bridge Project Funding Examples August 12, 2026
MAH-Market St. Bridge over Mahoning River & NS & CSXT RR

## Slide 51
Bridge Project Funding Examples August 12, 2026
County Engineer Mark Eicher, P.E., P.S.
Maintenance Responsibility 528 Miles of Roadway (Centerline) 398 Structures
Bridge Projects With Outside Funding - Last 10 Years 1 Local Major Bridge Program 1 Ohio Publics Works (OPWC) 1 Accelerated Innovation Deployment (AID) 13 Local Bridge Program (LBR/BFP) (5 More Funded FY27-31)
Muskingum County

## Slide 52
Duncan Falls / Philo Bridge Replacement Project
Bridge Project Funding Examples August 12, 2026
OLD BRIDGE (TWO STRUCTURES)
7 SPANS - 828 FT LONG (Piers-1875, Superstructure-1979) 3 SPANS - 130 FT LONG (1953)
NEW BRIDGE (ONE STRUCTURE)
7 SPANS - 862 FT LONG (2018-2021)

## Slide 53
Duncan Falls / Philo Bridge Replacement Project
Bridge Project Funding Examples August 12, 2026
Project Challenges Funding, Funding, Funding
Bridge Location
Historic Significance
Right of Way
Utility Relocations
Muskingum River
Coordination

## Slide 54
Duncan Falls / Philo Bridge Replacement Project
Bridge Project Funding Examples August 12, 2026
Bid Price = $9,984,026 (Final = $12,633,026) | Federal Match | Federal Funds | Credit Bridge | Local Match | Local Funds | Total
Preliminary Engineering | 80% | $261,108 |  | 20% | $65,277 | $326,385
Environmental & Design Engineering, R/W Services | 80% | $1,106,410 |  | 20% | $276,602 | $1,383,012
R/W Acquisition & Utility Relocation | 95% | $1,600,000 | $300,000 | 5% | $100,000 | $2,000,000
CEAO – LBR Construction | 80% | $262,715 |  | 20% | $65,679 | $328,394
CEAO – LBR Construction Inspection & Engineering | 80% | $854,815 |  | 20% | $213,704 | $1,068,519
Local Major Bridge - Construction | 95% | $11,689,400 |  | 5% | $615,232 | $12,304,632
Local Funded - Construction Engineering & Inspection |  |  |  | 100% | $78,022 | $78,022
Grand Total |  | $15,774,448 | $300,000 |  | $1,414,516 | $17,488,964
$4,085,048
CEAO LBR Funding
$11,689,400
Local Major Bridge Funding
$300,000
Credit Bridge
$916,130
SIB Loan
$498,386
Local Funds
$17,488,964
Total Cost

## Slide 55
Duncan Falls / Philo Bridge Replacement Project
Bridge Project Funding Examples August 12, 2026

## Slide 56
Duncan Falls / Philo Bridge Replacement Project
Bridge Project Funding Examples August 12, 2026
2019 FHWA Excellence in Right of Way Award
2022 ACEC Partnering Award

## Slide 57
Gaysport Bridge Replacement Project
Bridge Project Funding Examples August 12, 2026
OLD BRIDGE (ONE STRUCTURE)
7 Spans - 686 ft (Piers-1886, Superstructure-1971)
NEW BRIDGE (ONE STRUCTURE)
7 Spans - 686 ft (2022-2024)

## Slide 58
Gaysport Bridge Replacement Project
Bridge Project Funding Examples August 12, 2026
Project Challenges Funding, Funding, Funding
Bridge Location
Historic Significance
Right of Way
Utility Relocations
Muskingum River
Coordination

## Slide 59
Gaysport Bridge Replacement Project
Bridge Project Funding Examples August 12, 2026
Bid Price = $6,855,410 (Final = $7,370,994) | Federal Match | Federal Funds | Credit Bridge | Local Match | Local Funds | Total
Preliminary Engineering (STS & Hydraulics) & R/W Acquisition | 0% |  |  | 100% | $78,757 | $78,757
Environmental & R/W Services (Task Order) | 100% | $267,702 |  | 0% |  | $267,702
Design Engineering | 0% |  |  | 100% | $21,750 | $21,750
CEAO - LBR Construction | 80% | $5,484,328 |  | 20% | $1,371,082 | $6,855,410
CEAO - LBR Construction Inspection & Engineering | 80% | $383,902 |  | 20% | $95,976 | $479,878
CPF - Construction | 80% | $412,593 |  | 20% | $103,147 | $515,740
Local Funded - Construction Engineering & Inspection | 0% |  |  | 100% | $32,105 | $32,105
Grand Total |  | $6,548,525 |  |  | $1,702,817 | $8,251,342
$5,868,230
CEAO LBR Funding
$412,593
Community Project Funding
$1,507,163
SIB Loan
$195,654
Local Funds
$8,251,342
Total Cost

## Slide 60
Gaysport Bridge Replacement Project
Bridge Project Funding Examples August 11, 2026

## Slide 61
Gaysport Bridge Replacement Project
Bridge Project Funding Examples August 12, 2026
2024 Historic Bridge Preservation
Sustainable Design Award

## Slide 62
Thompson Road Bridge Replacement
Bridge Project Funding Examples August 12, 2026
OLD BRIDGE
1 SPAN - 56 FT LONG
NEW BRIDGE
1 SPANS - 56 FT LONG

## Slide 63
Thompson Road Bridge Replacement
Bridge Project Funding Examples August 12, 2026
Bid Price = $343,909 | OPWC Match | OPWC Funds | Credit Bridge | Local Match | Local Funds | Total
Construction | 74% | $240,500 |  | 26% | $103,409 | $343,909
Eligible Cost = $337,532 |  |  |  |  |  | 
Credit Amount Approved (80%) |  |  | $270,025 |  |  | 
Net Project Cost = - $166,616 |  |  |  |  |  | 

## Slide 64
Panel Questions ???
Bridge Project Funding Examples August 12, 2026